## Slide 1: Advanced Topic in Communication System: Broadband Optical Networks
4 December 2015
Delivered by Dr Erna Sri Sugesti

## Slide 2: It’s started from this
Hot for 2014: Virtualization in the optical transport network
By Brandon CollingsIn data centers, network function virtualization is in full swing as firewalls, load balancers, and routers are increasingly software-implemented on diverse, cloud-enabled hardware elements. This trend has dramatically increased the value data center operators extract from their investments. Meanwhile, metro and long-haul optical transport networks are being built with next-generation ROADM features that promise substantial gains in capacity, flexibility, and operational efficiency. In 2014, as with virtualization within data centers, control-plane-enabled virtualization of the optical network will simplify life for network operators considerably. The key difference between control-plane virtualization in transport networks and data center software-defined networking (SDN) is in what is actually getting virtualized. SDN is typically thought of in terms of taking network functions away from standalone, discreet hardware platforms and instead managing these elements as virtual machines. Control-plane virtualization in transport networks will generalize and simplify network functions and actions: masking off physical-plane details and automating planning, configuration, management, optimization, and healing. The human operator and planning processes are what will be virtualized. This increased automation and flexibility will let operators unload work off of upper layers and put it on lower levels, including the photonic level. For example, today, in a non-automated network, protection against node failure is handled by costly multiple redundant systems. Automated networks relax the need for expensive, extensive redundancy by automatically re-routing around network faults and restoring traffic. Virtualization will enable the rapid deployment of new services across the network. Operators will simply instruct the management system with the needed parameters of the new service—at the service level. The control plane will then, in an optimal way, determine the underlying physical requirements needed to support the service. A simple request to the control plane will replace what was a highly-manual, lengthy, expensive, revenue-risking, and fault-prone process. So, 2014 will be a year of sorting out how this virtualization/SDN will be implemented in next-generation optical networks that are just coming online. The potential is there to enable services to be turned up much faster, operators with less training to use mouse clicks instead of engineering processes to do their jobs, faults to be accommodated immediately, and in general, to do much more with much less. The chief obstacle to this virtualization trend is the cautiousness with which the big carriers will approach this software development, control-plane integration, and increased level of control-plane management of their networks. It is a shifting paradigm, like convincing a pilot to move from flying with a control stick to “flying by wire.” 2014 will see a big ramp-up for rollouts, but implementing virtualization will come in fits and starts. Brandon Collings, Ph.D, is CTO within the Communications and Commercial Optical Products business unit of JDSU.
http://www.lightwaveonline.com/blogs/lightwave-guest-blog/2014/02/hot-for-2014-virtualization-in-the-optical-transport-network.html

## Slide 3: Next-Generation Inter-Data Center Networking
ECOC Special Symposia2
Next Generation Data Centres - Paving the way for the Zettabyte Era
Chris Liou – Vice President, Network Strategy

## Slide 4: Data Center Networking Observations
Not all inter-DC networking is the same
What’s different?
  DC sites & topology – quantity, location, distance, size
  Evolving traffic patterns
    Applications – cloud, grid, IaaS, content
    Volume, uniformity, duration, QoS
  Traffic peak & avg, flow characteristics as a function of time
Perceived value of dynamic bandwidth varies
  Broad spectrum of use-cases for optical WAN
  High correlated with business model, economics (fiber, network) & operational expertise
Simplified operations is universal
  OpEx costs drive significant fraction of TCO
  Flexibility & control over optical bandwidth without the PhD
Notes: TCO = total cost ownership  Total cost of ownership (TCO) is an estimation of the expenses associated with purchasing, deploying, using and retiring a product or piece of equipment.

## Slide 5: A Perspective on Core Network requirements for Cloud
Restoring bandwidth quickly and cost effectively
Minimize impact from both single & multiple simultaneous failure scenarios
Milliseconds matter (user conversion rates, customer retention)
Intelligence in the network to optimize latency for particular application
Priorities for different classes of cloud services
Avoid application-level timeouts
Capacity for unpredictable, unplanned & one-time events
Rapid scale of on-demand cloud services (up & down) in minutes
Resiliency
Rapid Bandwidth Delivery
Low Latency

## Slide 6: Key DC WAN Networking Challenges
Scalability Convergence Automation
Traffic Evolution
Cloud. Big Data. Big Science.
High bandwidth flows, dynamicism, transience, churn.
Speed & Efficiency
Instant demand fulfillment.
Programmable control.
Efficient resource utilization
Growing complexity
Racks, fibers, power, space.
Planning, operations, teams.

## Slide 7: The Evolving Optical Core
Data Center & Virtualization
Industry moving to 100Gb coherent technology
Capacity & Bandwidth Management
Network layer convergence simplifying networks (WDM/OTN/Packet or any mix needed)
Emerging SDN solutions enable re-architecture of the network
Intelligent traffic mgmt & engineering enabling new flexibility, new architectural options
Optical Super-channels & Flexible Grid emerging
Age of Virtualization – storage, compute, network
Integration & orchestration of Network & IT
Core Optical
Technologies
Ethernet service rates increasing, but services no longer equivalent to ls
Varying, often dynamic, traffic patterns & profiles

## Slide 8: Scaling Capacity & Interfaces
Ethernet interconnect dominant
DC-DC Interconnect needs vary
N x 10, 40, 100GbE demands commonplace
400GbE standardization in progress
IEEE 802.3 Report: 1(+) TbE by 2020
Can platform refresh be avoided?
Super-channels maximize fiber capacity
Flexible Grid for spectral efficiency
FlexCoherent™ for reach / capacity
Single card
1T QPSK
Long-haul
Expanded spectrum beyond C-band.
Fiber networks evolving to super-channels, whilst inter-DC bandwidth
will vary & evolve, based on need & economics.

## Slide 9: Enhanced Fiber Performance with FlexCoherent
BPSK
+ Coherent Detection
1 bit per symbol
QPSK
2 bits per symbol
16QAM
4 bit per symbol
PM-16QAM
PM-QPSK
PM-BPSK
Capacity
Reach
“You Cannot Move Cities Closer Together”
Balance between network economics & fiber capacity is required

## Slide 10: Increasing Spectral Efficiency Flexible Grid Super-Channels
50GHz, Fixed Grid
1Tb/s PM-QPSK = 500 GHz
Fixed Grid
  Coherent transmission
  Single operational cycle
  Seen as one pool of capacity
  Compatible with legacy WSS ROADMs
Flexible Grid
  Coherent transmission
  Single operational cycle
  Seen as one pool of capacity
  Requires flexible grid ROADMs
  25% more efficient use of spectrum*
Flexible Grid
1Tb/s PM-QPSK = 375 GHz
*Comparing QPSK to QPSK
Flexible Grid expands C-band capacity by ~25%

## Slide 11: Extending Accessible Spectrum
6.4T
8.0T
9.5T
24T
80 x 100G
9.5Tb/s
24 x 1T
24 Tb/s
21T
12T
21 x 1T
16 x 500G
21 Tb/s
Fixed Grid Channels
FlexChannels
Extended C Band Amp Chain
C Band Amp Chain
19 x 500G
Accessing additional spectrum (eg, L-band) can further increase capacity.

## Slide 12: Inter-DC Capacity & Bandwidth Management
Optical transmission evolving towards super-channels to address capacity
  C+ band yields ~24 x 1Tb 16QAM channels, 12 1Tb QPSK channels
  Fewer manageable optical bandwidth units per fiber
Is optical and/or digital switching valued?
  It depends …
  Topology, applications, traffic flows, bandwidth usage
  Relative economics
  Organizational expertise
  Resiliency requirements…and more
What approaches are there for managing capacity and bandwidth?

## Slide 13: Toolkit for Flexible Multi Layer Bandwidth Management
Optical Capacity Management
  Flexible grid WSS down to 50GHz with 12.5GHz granularity
  Dynamic add/drop/express of Contiguous and Split-Spectrum Super-Channels
Digital Bandwidth Management
  Multi-Tb switching capacity
  Unconstrained switching flexibility down to ODU0/ODUflex level
  Native Packet Switching
    Ethernet PW over OTN
    Mid-point LSR with MPLS(-TP)
Core P-OTN
Digital Bandwidth Management
Packet
LSP
OTN ODUk/ODuFlex
  Optical Express of super-channels for
  CapEx savings
    Multi-layer bandwidth mgmt provides options for
    optimizing mix of digital & optical switching
Optical super-channels

## Slide 14: Evolving Landscape for Network Resiliency
Shared bandwidth, Transport layer
More Reliable
Sub 50ms recovery on failure
Multi-failure recovery scenarios
Minimal
Costs
Packet IP/MPLS: MPLS Fast Re-Route (FRR)
Sub 50ms for limited scenarios
Multi-failure recovery scenarios
Shared bandwidth, Packet layer $$$
Digital OTN: Hardware based Shared Mesh Protection
Sub 50ms recovery on failure
Multi-failure recovery scenarios
Shared bandwidth, Transport layer
Less Cost
Fast
Recovery
SONET/SDH/ETH/OTN: 1+1 Protection
Single failure recovery scenario
Dedicated backup resource
Sub 50ms recovery on failure
Digital : Software Mesh Restoration
Up to a few seconds recovery on failure
Multi-failure recovery scenarios
Shared bandwidth, Transport layer
Multi-failure backups
Sub 50ms recovery on failure
Optical Link Protection: 1+1 Protection
Single OLOS failure recovery scenario
Dedicated backup Fiber Link
Up to a few seconds recovery on failure

## Slide 15: IP/MPLS FRR vs. Shared Mesh Protection (SMP) - IP/MPLS Level Restorations
Transport
IP
IP
IP
IP
IP
IP
Data Path
IP/MPLS Path
The Ports Between Intermediate Router & Transport Are Not Free

## Slide 16: IP/MPLS FRR vs. Shared Mesh Protection (SMP) - Transport Level protection with SMP
Transport
IP
IP
IP
IP
IP
IP
Data Path
IP/MPLS Path
FRR back off
FRR back off
Network savings achievable via reduction in router ports

## Slide 17: Extending SDN to Transport Network Programmability & Abstraction
Network Services Applications
Multi-layer, Multi-vendor, Multi-domain
Carrier SDN Controller
Network Virtualization
IT/Cloud
Orchestration
Business
Applications
Other
SDN Control Solutions
Application NBI
On-demand Bandwidth
Simplify/Automate Operations
Improve Resource Utilization
Speed New Service Deployment
SDN Control,
Virtualization &
Applications
Data Center
Converged P-OTN
Packet, OTN, Optics
evolution
ONF OTWG
OIF Carrier WG

## Slide 18: Transport SDN Drivers for Data Center Networking
Network virtualization (L1 O-VPN)
  L1 O-VPN network overlays for multi-tenancy on optical network
Programmability for enhancing on-demand networking
  Dynamic Virtual Network Topology
Packet layer <-> P-OTN integration & coordination
  Enhanced cloud performance
  Improve network resource efficiency through adaptive behavior
Unifying control plane technology
  Simplify operations
Multi-layer network optimization & resiliency
  Joint consideration of multiple layers through global view
    Initial standardization efforts underway (e.g., ONF, OIF)

## Slide 19: Summary
Data center networking is not all the same
Optical networking landscape rapidly evolving
  Divergence of bandwidth service rates from super-channel capacity
  Efficient utilization of wavelengths essential to many
Convergence of networking layers essential for simplifying networks & reducing costs
  New converged transport capabilities challenging status quo
Transport SDN enables automation & programmability but requires abstraction
  Focus leaning towards programming bandwidth services, not components/technologies